## Slide 1
USE CASE REVIEW
SDN-Based QoS Management
for Video Streaming
How Software Defined Networking can dynamically manage Quality of Service for video streaming
Course: Software Defined Networks (SDN)
Presented by:
Your Name · Roll No. · Team members
Department / University:
Dept. of Computer Science & Engineering
Notes: Good morning. Our use case review is on SDN-based QoS management for video streaming. The one-line framing of the whole talk: video is the largest and most delay-sensitive traffic class on the internet, but the network that carries it is still best-effort. Our question is whether Software Defined Networking - because it gives us a centralised, programmable control plane - can manage Quality of Service for video dynamically, instead of through static, box-by-box configuration. The review has four parts: the problem, why SDN is the right tool, our objectives, and what the literature already shows - ending with the research gap and a proposed framework.

## Slide 2
Problem Statement: Video Meets a Best-Effort Network
WHY QoS MATTERS MOST FOR VIDEO
1
Demand keeps climbing Video dominates internet traffic; HD, 4K and live streaming raise the bitrate floor every year.
2
Bandwidth is not stable Available capacity fluctuates with load; bottleneck links congest at peak hours.
3
QoS degrades in four ways Latency, jitter, packet loss and throughput variation - all four hit video at once.
4
The user feels it immediately Rebuffering, bitrate switching, long startup delay, visible artifacts.
5
Conventional management is too slow Static DiffServ / IntServ classes, per-device CLI configuration, no network-wide view or fast reaction.
Video is high-volume, delay-sensitive and continuously consumed - so it is the traffic class that suffers first when QoS is left to chance.
NETWORK SYMPTOM
WHAT THE VIEWER SEES
Congestion /
bandwidth drop
Bitrate drops, then
rebuffering
High end-to-end
latency
Long startup delay,
laggy live streams
Jitter
(delay variation)
Playout stalls, audio-
video desync
Packet loss
Blockiness, artifacts,
frame freeze
QoS metrics (network level) → QoE (user level)
Notes: Start with scale: video is the single largest share of internet traffic, and the quality bar keeps rising - HD, 4K, live. The core difficulty is a mismatch. Video needs a sustained, steady, low-jitter flow, but IP networks are best-effort: every packet is treated the same, and available bandwidth changes minute to minute as other users share the bottleneck link. Walk the right-hand table - this is the key teaching point. Four network-level QoS metrics each map to something the viewer actually notices. Congestion causes the player to drop bitrate and eventually rebuffer. High latency shows up as startup delay. Jitter causes the playout buffer to run dry, so the video stalls. Packet loss produces visible artifacts and frozen frames. Finally, why conventional management is not enough: DiffServ and IntServ give you static traffic classes that must be configured device by device, with no global view of the network and no fast feedback loop. If congestion appears on a link in the middle of a stream, nothing reconfigures itself. That is exactly the gap SDN addresses.

## Slide 3
Motivation: Why SDN Fits This Problem
PROGRAMMABLE CONTROL + NETWORK-WIDE VIEW
Video
Streaming Traffic
Network
Monitoring
SDN
Controller
QoS
Decision
Flow Rules
(OpenFlow)
Network
Devices
Closed control loop: the controller keeps measuring and keeps re-deciding while the video is still playing.
What SDN gives us
Control plane separated from the data plane - forwarding logic moves out of the switch
Centralised, network-wide view of topology, links and load
Programmability through northbound APIs (Ryu, ONOS, OpenDaylight)
Real-time monitoring from OpenFlow port and flow counters
What we can do with it for video
Classify and prioritise video flows into dedicated queues
Dynamic QoS routing and rerouting around congested links
Per-flow bandwidth allocation, metering and rate limiting
Close the loop on QoE - measure, decide, enforce, re-measure
Notes: The flow at the top is the whole idea in one line. Video traffic enters the network; the controller monitors conditions; it makes a QoS decision; that decision becomes flow rules pushed down to the switches, which then treat video differently. Note the two highlighted boxes - controller and QoS decision. That is where the intelligence lives, and it is exactly what a traditional network does not have in one place. Left column - the SDN properties we are relying on. Because control is decoupled from forwarding, the controller can see the whole topology rather than one hop. Because it is programmable, our QoS policy is application code, not per-switch CLI. And because OpenFlow switches export port and flow counters, we get near real-time measurements for free. Right column - what those properties buy us for video specifically: classify video into a priority queue, reroute it around a congested link, cap competing traffic, and repeat. The last bullet is the important one - QoE improves because the loop closes continuously, not because one configuration was correct at setup time.

## Slide 4
Use Case Selection and Objectives
SCOPE, JUSTIFICATION AND WHAT WE AIM TO ACHIEVE
Why this use case?
Video is the largest and most quality-sensitive traffic class in campus, ISP and enterprise networks.
Its requirements are measurable - delay, jitter, loss, throughput - so QoS policy can be evaluated objectively.
Static QoS classes cannot follow traffic that changes second by second.
Adaptive players react only at the client; they cannot see or fix the bottleneck.
SDN adds the missing piece: a controller that sees the network and can act on it.
Objectives
O1
Monitor link load, delay, jitter and loss continuously from the controller
O2
Detect congestion and performance degradation on active video paths
O3
Classify and prioritise video flows over background traffic
O4
Allocate bandwidth dynamically and reroute flows when a path degrades
O5
Reduce packet loss, latency, jitter and rebuffering events
O6
Improve measured video QoE, not just raw network numbers
QoS - network level: delay, jitter, packet loss, throughput, link utilisation. What the controller can measure and control.
QoE - user level: startup delay, stall count and duration, bitrate switches, perceived quality (MOS, SSIM, VMAF).
Notes: First justify the choice of domain. Video was selected for three reasons: it is the dominant traffic class, its requirements are precisely measurable, and it degrades in ways users notice instantly - which makes it a good test of any QoS mechanism. Then the honest limitation of today's solutions. Adaptive bitrate players are client-side only: a DASH player can lower its quality when it senses trouble, but it cannot see which link is congested, cannot reroute, and cannot stop a competing download from taking the bandwidth. Static QoS classes have the opposite problem - they are in the network but they never adapt. Then read the six objectives. They form a pipeline: measure, detect, prioritise, allocate or reroute, reduce impairments, and finally improve QoE. The bottom strip is worth pausing on, because examiners often ask about it. QoS is what the network measures - delay, jitter, loss, throughput. QoE is what the user experiences - startup delay, stalls, quality switches, perceived quality scores like MOS, SSIM or VMAF. Better QoS usually improves QoE, but not always: a stream can meet its delay and loss targets and still look bad if the player oscillates between bitrates. That gap is the reason this use case is still an open research area.

## Slide 5
Literature Review I - Foundations of SDN-Based Video QoS
CONTROLLER-DRIVEN QoS ROUTING AND NETWORK-ASSISTED STREAMING
1
OpenQoS: An OpenFlow controller design for multimedia delivery with end-to-end QoS
Egilmez, Dane, Bagci & Tekalp — APSIPA ASC, 2012
Problem: Best-effort routing gives no quality guarantee to multimedia flows.
Approach: An OpenFlow controller places video on dynamically optimised QoS routes (loss-based metric, LARAC), while other traffic keeps the shortest path; links are polled so congested paths are recomputed.
Findings: Seamless delivery with little or no visible artifact, and no adverse effect on the other traffic classes.
Relevance: The foundational proof that controller-driven QoS routing works for video.
2
Delivering stable high-quality video: an SDN architecture with DASH assisting network elements
Kleinrouweler, Cabrero & Cesar — ACM MMSys, 2016
Problem: Competing DASH clients on a shared bottleneck produce unstable quality and freezes.
Approach: SDN-based assisting network elements signal a target bitrate to each player and shape the bandwidth given to it.
Findings: Markedly more stable, higher and fairer quality across clients; scaled in later work to hundreds of concurrent players.
Relevance: Shows the network can guide the player instead of competing with it.
3
SDNDASH: Improving QoE of HTTP adaptive streaming using software defined networking
Bentaleb, Begen & Zimmermann — ACM Multimedia, 2016
Problem: Client-driven HAS causes unfair bandwidth competition, quality oscillation and under-utilisation.
Approach: An SDN architecture for dynamic, per-client resource allocation and QoE management at the controller.
Findings: Per-client QoE improved by at least 30%, and up to 80% more clients supported at the same QoE.
Relevance: Quantifies the QoE gain achievable from SDN-side control.
References [1] H. E. Egilmez, S. T. Dane, K. T. Bagci, A. M. Tekalp, APSIPA ASC 2012. [2] J. W. Kleinrouweler, S. Cabrero, P. Cesar, ACM MMSys 2016, pp. 4:1-4:10, doi:10.1145/2910017.2910599. [3] A. Bentaleb, A. C. Begen, R. Zimmermann, ACM MM 2016, pp. 1296-1305, doi:10.1145/2964284.2964332.
Notes: Three papers, in order of what they contributed. OpenQoS, 2012, is the foundational work and still the standard reference. Egilmez and colleagues split traffic at the controller: multimedia flows get a QoS-optimised route computed with a loss-aware metric, everything else keeps the shortest path. The controller polls link state, so when a path congests it recomputes. Two things to highlight - video was delivered with almost no visible artifacts, and crucially the other traffic was not harmed, which was a weakness of earlier QoS designs. Kleinrouweler 2016 attacks a different failure. When several DASH players share one bottleneck, each one independently probes for bandwidth, and they fight - quality oscillates and streams freeze. Their answer is a DASH-assisting network element: the network tells each player what bitrate it can actually sustain, and shapes bandwidth to match. The result is stable, fairer quality. This paper won the DASH-IF Excellence in DASH award. SDNDASH, also 2016, is the one to quote for numbers: per-client QoE improved by at least 30 percent, and the same network supported up to 80 percent more clients at equal QoE. That is the strongest quantitative evidence that SDN-side control pays off. The pattern across all three: move some decision-making from the client into the controller, because only the controller can see the whole network.

## Slide 6
Literature Review II - Synthesis and Research Gap
FROM STATIC POLICY TO LEARNING-BASED QoS CONTROL
4
VQoSRR: Video streaming adaptive QoS routing with resource reservation for SDN
Elbasheer, Aldegheishem, Alrajeh & Lloret — Electronics (MDPI), 2022
Combines QoS-based route computation with queue-based resource reservation, and shifts a flow to an alternative path when QoE is violated. Reported effective control over both routes and resources, with video quality maintained.
5
A reinforcement learning-based routing for real-time multimedia traffic over SDN
Al Jameel, Kanakis, Turner, Al-Sherbaz & Bhaya — Electronics (MDPI), 2022
An RL agent explores and learns paths for video flows inside the SDN environment, rather than following a fixed metric. Evaluated under low and high load using VMAF and SSIM - i.e. judged on perceptual quality, not only on QoS counters.
6
QoE-driven adaptive video streaming: architectures, techniques and future challenges toward 6G
Alsader, Barakabitze & Mkwawa — IEEE Access, 2025
Recent survey of QoE-driven streaming across SDN, NFV and MEC with AI/ML and cloud-edge architectures. Confirms that real-time QoE monitoring and resource allocation across diverse services remain open problems.
What the literature agrees on
Common pattern: monitor → classify → prioritise → route or reserve → enforce flow rules
Metrics optimised: delay, jitter, loss, throughput; increasingly QoE (MOS, SSIM, VMAF, stalls)
Tooling: OpenFlow with Ryu / ONOS / OpenDaylight, queues and DSCP marking, Mininet testbeds
Strength: consistent, measurable gains over best-effort baselines
Research gap
Adapting QoS decisions fast enough for traffic that changes second by second
QoS targets met, yet QoE still poor - the mapping between them is not solved
Scalability of centralised control: monitoring overhead and controller load
Heterogeneous video and access networks need policies that generalise, not hand-tuned thresholds
References [4] M. O. Elbasheer et al., Electronics 11(8):1252, 2022, doi:10.3390/electronics11081252. [5] M. Al Jameel et al., Electronics 11(15):2441, 2022, doi:10.3390/electronics11152441. [6] M. Alsader, A. A. Barakabitze, I.-H. Mkwawa, IEEE Access 13:157408-157441, 2025.
Notes: This slide is a synthesis, so present the trend rather than three separate summaries. VQoSRR, 2022, is the engineering-complete version of the 2012 idea: QoS routing plus explicit resource reservation using switch queues, and a re-routing algorithm that fires when QoE is violated. Note the shift - the trigger is a QoE violation, not just a link metric. Al Jameel 2022 is the shift in method. Instead of a hand-designed routing metric, a reinforcement learning agent learns which paths serve video best by interacting with the SDN environment, and it is evaluated with VMAF and SSIM - perceptual quality measures. That is the move from static policy to learned policy. The 2025 IEEE Access survey confirms this is where the field is heading - QoE-driven control across SDN, NFV and MEC with AI and ML - and it explicitly lists real-time QoE monitoring and multi-service resource allocation as still-open problems. Now the gap, and be careful to claim only what the papers support. First, reaction speed: OpenQoS polled roughly once per second, and later work still trades monitoring frequency against overhead. Second, the QoS-QoE mapping: several of these papers show good network metrics can coexist with a poor viewing experience. Third, scalability of centralised control - more monitoring means more controller load. Fourth, generality: thresholds tuned on one testbed do not transfer to another network or another video mix. Those four points, taken together, are what motivates an intelligent, closed-loop QoS framework.

## Slide 7
Proposed Use Case Framework and Takeaways
MEASURE · DECIDE · ENFORCE · RE-MEASURE
SDN CONTROLLER · CONTROL PLANE
Monitoring &
Statistics
port / flow counters,
delay, jitter, loss
QoS Decision
Module
detect congestion,
choose path & queue
Flow Rule
Enforcement
install / update
OpenFlow rules
flow rules
statistics
DATA PLANE · OPENFLOW SWITCHES
Video
Clients
Switch
Switch
Switch
Streaming
Server
Video flows are classified, queued and routed by rules the controller writes while the stream is running.
Expected outcome
Better bandwidth utilisation
Lower latency, loss and jitter
Fewer and shorter rebuffering events
Higher, steadier video QoE
Key takeaways
1
Video streaming exposes the limits of best-effort networking; QoS must be continuous, not configured once.
2
SDN supplies exactly what was missing - a network-wide view plus programmable, per-flow enforcement.
3
The open problem is intelligence and scale: mapping QoS to QoE and adapting fast without overloading the controller.
Full reference list [1]-[6] on slides 5 and 6.
Notes: This is the framework we propose for the use case, and it is deliberately assembled from what the literature already validated rather than invented from scratch. Bottom half, the data plane: video clients, a streaming server, and OpenFlow switches in between. Nothing here decides policy - the switches only forward according to the rules they hold. Top half, the control plane, has three modules. Monitoring collects port and flow counters and derives delay, jitter and loss. The QoS decision module - the highlighted box - detects congestion or degradation and chooses a path and a queue for each video flow. Flow rule enforcement installs or updates the OpenFlow rules. The two arrows are the point of the whole design. Statistics flow up, flow rules flow down, and this repeats while the video is still playing. That closed loop is what a traditional configured network cannot do. Expected outcome: better use of available bandwidth, lower latency, loss and jitter, fewer rebuffering events, and a higher and steadier QoE. Close on the three takeaways. Video exposes the limits of best-effort delivery, so QoS has to be continuous rather than configured once. SDN provides the two missing ingredients - a global view and programmable per-flow enforcement. And the remaining research problem is intelligence and scale: mapping network QoS onto user QoE, and adapting quickly without overloading a centralised controller. That last point is where our future work would go. Thank you - happy to take questions.